## Slide 1: Design and Analysis of Gear Box Shaft
Course: Strength of Materials (ME2303)
Batch: E-3Guide: Dr. Dinesh Washimkar
Submitted by:
54 Shantanu Sasane | 59 Harshal Shinde | 64 Rahul Patil
66 Ahmed Shaikh | 67 Shantanu Shewale | 68 Vinit Takate
Department of Mechanical Engineering
Vishwakarma Institute of Technology, Pune
Sem III, AY 2025–26

## Slide 2: Project focuses on structural and torsional behavior of a differential gearbox shaft.
Abstract
Model created using Fusion 360 and analyzed in ANSYS 2025 R2.
Results: Max Stress ≈ 1.5223+008 Pa, Max Deformation ≈ 1.1106e- 004 m.
Analytical, programming, and simulation results matched within
±5%,
confirming design safety under the given load conditions.

## Slide 3
Introduction
Gearbox shafts transmit power and experience bending, torsion, and shear.
Goal: Ensure strength and stiffness under combined loading.
Methods used: CAD modeling, analytical calculations, and FEA validation in ANSYS.
Results confirmed safe and reliable design performance.

## Slide 4: Problem Statement
To design and analyze a differential gearbox shaft subjected to torque and bending due to gear forces, and to verify stresses and deformation using analytical methods, programming, and FEA.

## Slide 5: 1. Model gearbox shaft accurately using Fusion 360.
Objectives
2. Perform FEA in ANSYS under applied load.
3. Calculate deformation & stress; check material suitability.
Validate results using programming (Python/Excel/C++).
Apply SOM concepts: stress, torsion, bending, deformation.

## Slide 6: CAD Modeling
Geometry modelled usingFusion 360.
Steps:
1. Revolve base sketch to form shaft.
2. Apply circular pattern (22 splines).
3. Mirror operation for symmetry.

## Slide 7
In this project, the gearbox shaft was designed using Autodesk Fusion 360.
We first created a 2D sketch based on actual dimensions, including total shaft length, diameters, spline width, keyway depth, and fillet radius.
After fully constraining the sketch, we used the revolve tool to generate a 3D solid shaft.
The splines were created using extruded cuts and then patterned using the circular pattern feature with 22 repetitions.
A mirror operation was used to maintain symmetry.
Chamfers and 1 mm fillets were added to remove sharp edges and reduce stress concentration, which is important from a Strength of Materials perspective.
The final model was exported as a STEP/STL file for FEA analysis in ANSYS.

## Slide 8
Here are the key SOM-based decisions for my differential shaft:
• Fillets: Used to reduce stress concentration and prevent fatigue.
• Diameter: Calculated to get the right polar moment of inertia (J) for handling torsion.
• Splines: Added to maximize torque transmission capacity.
• Chamfering: Applied to the ends to avoid crack initiation.
• Length/Thickness: Balanced to ensure rigidity and control deflection.
• Material: I used Structural Steel, selected for its high stiffness (210 GPa Young's Modulus) and reliable yield strength (250 MPa).

## Slide 9: ANALYSIS
Fillet applied to reduce
stress concentration.
Final 3D model ready for analysis and exported to ANSYS.

## Slide 10: Material Selection
Material: Structural Steel
E = 2 × 10⁵ MPa | G = 7.7 × 10⁴ MPa | σᵧ =
250 MPa
Reason: High strength, easy availability, machinability, suitable for power transmission shafts.

## Slide 11: Programming Support
Calculated torsional shear stress, bending stress, and angle of twist.
Results matched with ANSYS (±5% error), validating theoretical equations.

## Slide 12: FEA Analysis Results
Solver: Static Structural (ANSYS 2025 R2)
Max Equivalent Stress: 1.5223e+008 Pa | Max
Deformation: 1.1106e-004 m
Stress concentrated near spline ends; design safe under given torque.

## Slide 13: Discussion
Max stress occurs at spline region due to stress concentration.
Deformation maximum at mid- span.
Analytical and FEA results consistent; redesign or stronger material suggested for safety.

## Slide 14: Conclusion
Gearbox shaft successfully designed and analyzed.
FEA results show stress near yield limit.
Confirms theoretical behavior of bending and torsion.
Further material or design improvements recommended.

## Slide 15: Thank You